## Slide 1
Secure Distributed VLM Inference
Experiment logic and interim findings
Goal: evaluate whether visual embedding transmission, encrypted channels, and Intel TDX can protect a split VLM workflow without making inference impractical.
edge
cloud
nanoVLM | split inference | HTTPS | Intel TDX
01

## Slide 2
CT5195 MASTER CAPSTONE
The question shifts from running the model to measuring security cost
Uploading raw images exposes sensitive visual content. Sending visual embeddings reduces direct image exposure, but embeddings can still leak information. The experiment therefore measures the performance cost of adding transport security and a trusted cloud runtime.
Privacy motive
Keep the raw image at the edge and send an intermediate representation instead.
Security additions
Protect embedding transport with HTTPS and protect cloud execution with TDX.
Experimental focus
Compare local, split, encrypted split, and TDX split inference on latency and CPU cost.
Central question: does stronger protection break the practical latency budget for VLM inference?
02

## Slide 3
CT5195 MASTER CAPSTONE
The system splits nanoVLM between edge vision encoding and cloud decoding
Image input
AI2D image
resize / split
Edge
vision encoder
projection module
Transport
embedding bytes
metadata header
Cloud
rebuild tensor
prompt tokens
Output
LLM decoder
generated text
Implementation basis: edge.py performs image preprocessing, visual embedding generation, and request sending. cloud.py receives bytes, reconstructs the tensor, combines it with prompt tokens, and runs the decoder.
The split point is after projection, so the cloud can generate text without receiving the raw image.
03

## Slide 4
CT5195 MASTER CAPSTONE
The experiment matrix isolates three comparison dimensions
Dimension
Control
Experiment
Purpose
Inference placement
Local baseline
Split inference
Measure the cost of splitting the model
Transport protocol
HTTP
HTTPS AES-GCM
HTTPS ChaCha20
Measure encryption and authentication overhead
Cloud environment
Standard VM
Intel TDX VM
Measure trusted execution overhead
Input batch
AI2D images
20 TDX images
Build repeatable interim metrics
The logic is sequential: first test split inference, then protocol choice, then TDX.
04

## Slide 5
CT5195 MASTER CAPSTONE
The metrics separate end-to-end latency into explainable stages
Split total latency
=
Edge compute
image preprocessing
vision encoder
projection
+
Transfer and cloud
payload transfer
cloud request
network overhead
+
Resource signals
edge CPU
cloud CPU
payload bytes
Payload
≈2.06 MB
Each image sends projected visual embeddings, not the original JPEG.
Protocol overhead
4-20 ms
HTTPS overhead is small compared with cloud generation time.
Cloud request
14.7-16.2 s
Current latency is dominated by model-side computation.
05

## Slide 6
CT5195 MASTER CAPSTONE
The current data suggests encryption is not the main bottleneck
Chart: 
| HTTP | AES-GCM | ChaCha20
Non-TDX split total | 31.88 | 31.76 | 32.16
TDX split total | 33.44 | 33.38 | 33.35
Average end-to-end split latency, seconds
Observation: within the same cloud environment, HTTP, AES-GCM, and ChaCha20 differ by less than 0.5 seconds end to end.
Interpretation: protocol overhead is measured in milliseconds. The larger cost sits in visual embedding generation and cloud decoder execution.
06

## Slide 7
CT5195 MASTER CAPSTONE
TDX overhead appears mainly in cloud request and CPU time
Chart: 
| HTTP | AES-GCM | ChaCha20
Non-TDX cloud request | 14.74 | 14.82 | 15.04
TDX cloud request | 16.23 | 16.15 | 16.13
Chart: 
| HTTP | AES-GCM | ChaCha20
Non-TDX cloud CPU | 29.48 | 29.64 | 30.08
TDX cloud CPU | 32.45 | 32.29 | 32.25
Cloud request time, seconds
Cloud CPU time, seconds
Current observation: TDX adds roughly 1.2-1.7 seconds to split total latency and about 2.2-3.0 seconds to cloud CPU time.
07

## Slide 8
CT5195 MASTER CAPSTONE
The findings are useful, but still interim
Finding 1
HTTPS AES-GCM and ChaCha20 do not create a visible end-to-end latency penalty in the current runs.
Finding 2
TDX has a larger measurable cost than the protocol choice, especially on cloud-side CPU time.
Finding 3
The split architecture is currently compute-bound rather than protocol-bound.
Caveats to state clearly
• Non-TDX and TDX runs use different sample counts: 25 and 20 images.
• The current summary emphasizes averages; variance, P95, throughput, and resource peaks should be added.
• Encryption, decryption, TLS setup, and key exchange should be timed separately instead of being folded into request latency.
08

## Slide 9
CT5195 MASTER CAPSTONE
Next experiments should close the security, performance, and correctness loop
01
Scale the runs
Use the same image count for TDX and non-TDX; report mean, standard deviation, and P95.
02
Split the timers
Measure serialization, encryption, decryption, TLS setup, cloud decoder, and edge encoder separately.
03
Validate outputs
Track matched and unmatched generations between split inference and the local baseline.
04
Optimize the path
Test embedding compression, float16 payloads, batching, or a lighter decoder for latency reduction.
09

## Slide 10
Bottom line
The experiment now has a testable route for secure split VLM inference: keep the raw image at the edge, transmit embeddings over protected channels, and run cloud decoding inside a trusted environment.
The strongest current message is that protocol encryption is not the dominant cost. The next research value comes from quantifying and reducing model-side and TDX overhead.
Next version: stronger statistics and finer-grained security overhead measurement.
10